## Slide 1
Dave Biersach
Brookhaven National Laboratory
dbiersach@bnl.gov
Survey of
Scientific Computing
(SciComp 301)
Session 05
2D Graphics,
Polar Coordinates

## Slide 2: Session Goals
Learn the SimpleScreen custom class to draw graphics
Understand the World bounding rectangle
Use Cartesian coordinates to draw 2D lines
Use polar coordinates to draw 2D circles
Approximate circles by dividing radians into intervals
Use a delay count to watch each interval being drawn
Appreciate the hidden geometry of the Olympic Rings
Draw fancy curves using parametric equations

## Slide 3: Cartesian Coordinates
Created by René Descartes in 1637

## Slide 4: Screen Pixels
A computer screen is divided into 2D array of small rectangles called pixels
Every pixels has both an X and a Y coordinate
Each pixel is set to a specific color
The number of pixels in each dimension is the resolution
Modern screens have resolutions greater than 1920 x 1080
The top left screen pixel has coordinates (0,0) and there are no negative pixel coordinates
Unfortunately there is an even greater discrepancy between Cartesian coordinates and pixel coordinates…

## Slide 5: Screen Y vs. World Y Coordinates
In screen coordinates, as you move from the top of the screen towards the bottom, the Y coordinate increases!
This is the exact opposite of world (Cartesian) coordinates
Fortunately, the X axis behaves the as expected between the screen and world coordinate system
This discrepancy will drive you nuts!

## Slide 6: World Bounding Rectangle
World coordinates are what we use when doing pure math
Screen coordinates are what we have to use when drawing
We need a way to map World X,Y to Screen X,Y
The world is framed by a “bounding rectangle” which is comprised of four variables of type double
  worldXmin, worldYmin
  worldXmax, worldYmax
The values for all four World variables are our choice – they can be as big or as small as we want them

## Slide 7: World Bounding Rectangle

## Slide 8: Screen Bounding Rectangle
The Screen bounding rectangle is the size of the Allegro display bitmap
Due to your smaller laptop screens, we set the size to be 501 x 501
Remember Screen Y coordinates are inverted as (0,0) is in the top left
(0, 500)
(500, 500)
(0, 0)

## Slide 9: Argb Color Encoding

## Slide 10: Alpha Blending = Opacity
Alpha = 0 means fully transparent (see through)
Alpha = 255 means fully opaque
We will be using Alpha = 255 in our code

## Slide 11: Various Colors in RGB Values

## Slide 12: Predefined Color “Names”

## Slide 13: Allegro Graphics Library
http://liballeg.org

## Slide 14: The SimpleScreen Class
Your App
SimpleScreen
Allegro

## Slide 15: The PointSet Class

## Slide 16: Open Lab 1 – Draw Triangle
No coding required – just follow along main()
Draw a 3-4-5 right triangle in the first quadrant
Paint the entire triangle RED including the interior
Set the correct world rectangle dimensions

## Slide 17: View Lab 1 – Draw Triangle

## Slide 18: View Lab 1 – Draw Triangle
(0, 0)
(4, 0)
(4, 3)

## Slide 19: View Lab 1 – Draw Triangle

## Slide 20: Run Lab 1 – Draw Triangle
To stop an Allegro app, close the backing terminal session FIRST

## Slide 21: Open Lab 2 – Draw Rectangle
Draw a violet rectangle in the first quadrant with the bottom left corner located at (0,0) and the longest side on the x-axis
The dimensions are: Area = 210 and Perimeter = 62
Assume the world coordinates are (-30,-30) to (30,30)

## Slide 22: Run Lab 2 – Draw Rectangle
This output is not what your scientist requested from you
(5, 5)
Draw a violet rectangle in the first quadrant with the bottom left corner located at (0,0) and the longest side on the x-axis
The dimensions are: Area = 210 and Perimeter = 62
Assume the world coordinates are (-30,-30) to (30,30)

## Slide 23: Edit Lab 2 – Draw Rectangle
Fix these last 3 points
Draw a violet rectangle in the first quadrant with the bottom left corner located at (0,0) and the longest side on the x-axis
The dimensions are: Area = 210 and Perimeter = 62
Assume the world coordinates are (-30,-30) to (30,30)
Edit the coordinates of the three remaining corner points with the correct values

## Slide 24: Check Lab 2 – Draw Rectangle
(21, 10)

## Slide 25: Polar Coordinates
A radius and an angle (theta)
make a 2D polar coordinate

## Slide 26: Polar Coordinates

## Slide 27: Polar Coordinates
Angles are measured in
radians
(0 ≤ θ ≤

## Slide 28: Open Lab 3 – Draw Circle
draw() is a “callback function” It is your custom drawing code that is called by the SimpleScreen object

## Slide 29: Run Lab 3 – Draw Circle
By using the callback pattern, the framework can call your custom draw() function whenever it needs to repaint the screen. This enables features like zooming
You can left click and drag on the canvas to outline a zoom frame. When you release the left mouse button it will set the new world rectangle to the coordinates of the zoom frame and redraw the image
A single right click will restore each of the prior zoom levels

## Slide 30: Edit Lab 3 – Draw Circle
First, change intervals to 8, run the app, then leave it at 8 for the next steps – what shape do you see?
Then change call to ss.DrawLines() as follows, and run the app each time after making these individual changes:
ss.DrawLines(psCircle, "red", 2, true, true);
ss.DrawLines(psCircle, "blue", 2, false);

## Slide 31: Creating a New Primitive

## Slide 32: Drawing the Olympic Rings
ringOffsetFullX
ringOffsetY
(0,0)
ringOffsetHalfX

## Slide 33: Open Lab 4 – Draw the Olympic Rings

## Slide 34: Run Lab 4 – Draw the Olympic Rings
To stop an Allegro app, close the backing terminal session FIRST
Where did all the other rings go?

## Slide 35: Open Lab 4 – Draw the Olympic Rings

## Slide 36: Check Lab 4 – Draw the Olympic Rings

## Slide 37: Parametric Curves

## Slide 38: Parametric Curves
The two parameters a, n are used to calculate the current radius as sweeps the circle

## Slide 39: Parametric Curves
Field Induced Polarization of Dirac Valleys in Bismuth*
*Bismuth is the element with the highest atomic mass that is stable

## Slide 40: Parametric Curves

## Slide 41: Parametric Curves
These two parameters are used to calculate the current radius as sweeps the circle
Open and run Lab 5

## Slide 42: Check Lab 5 - Parametric Curves
The key points are:
The radius is changing while is changing
The shape of the curve depends on two parameters

## Slide 43: Now you know…
Allegro is a free, open source, cross platform library for rendering 2D graphics
A “bounding rectangle” is used to scale world (virtual) coordinates to screen (physical) coordinates
How to create and populate elements of a PointSet
How to “connect the dots” using SimpleScreen.DrawLines()
How to use polar coordinates to draw 2D circles
We approximate circles by drawing small intervals
We can draw fancy curves by using parametric equations